## Slide 1: Sub-1 GHz Sensor to Cloud IoT Gateway
Adrian Ruiz

## Slide 2: Goal
Main Goal
  The goal of the project is to implement the Beagle Bone Black as a Sub-GHz Sensor Gateway
Objectives
  Ex: The goal(s) were accomplished by using two CC1350 launchpads. One CC1350 interfaces with the Beagle Bone Black while the other CC1350 reads sensor data and send it to the other CC1350. The data read recieved is passed to the BBB , and BBB will transmitt the data to the TI 15.4 Stack application.

## Slide 3: Outcome - Accomplishments
Outcome
  The onboard temperature sensor gathers data, and this data is sent the stack application
  Sending Sensor values is very beneficial.
    For example, the temperature can be used to determine if there is a fire going on.

## Slide 4: Components Used in Design
TI 15.4 Stack Linux Gateway SDK
  http://www.ti.com/tool/ti-15.4-stack-gateway-linux-sdk
Am335x-Linux Image
  http://software-dl.ti.com/processor-sdk-linux/esd/AM335X/latest/index_FDS.html
Beagle Bone Black
  https://beagleboard.org/black
CC1350
  http://www.ti.com/product/CC1350

## Slide 5: Tools used in Design
Code Composer Studio
  http://www.ti.com/tool/CCSTUDIO
Virtual Box
  https://www.virtualbox.org
Ubuntu
  https://www.ubuntu.com/download
Etcher
  https://etcher.io

## Slide 6: Schematics
One Launchpad gets data and sends it. The other Launchpad gets the data and passes it to the BBB. The BBB then uploads the data to the app.

## Slide 7: Pre-requisites used in Design
Prerequisites
  2x CC1350 and 1xBBB
  Virtual Machine with Ubuntu
  Arm-evm-linux image
Commands to install prerequisites
  $ sudo apt-get update && sudo apt-get upgrade
  $ scp bbb_prebuilt.tar.gz root@192.168.6.2:/home/root
  $tar –xvf bbb_prebuilt.tar.gz

## Slide 8: Implementation Details
Steps used in design for CC1350:
  Download Code Composer Studio
  Download Simple Link CC13x0_SDK library
  Import the Sensor example code from the \Examples\Dev tools\CC 1350 LaunchPad\TI 15.4 stack folder
  Import the Collector example code from the \Examples\Dev tools\CC 1350 LaunchPad\TI 15.4 stack folder
  Flash the one CC1350 with the Sensor code and flash the another one with the Collector code

## Slide 9: Implementation Details
Steps used in Design for Linux
  Download TI 15.4 Stack SDK to the ubuntu machine.
  Install the SDK
  Transfer the bbb_prebuilt.tar.gz to the BBB
Steps used in Design for BBB
  Flash the SD card with Linux image using Ethcer
  Boot off the SD card
  Find the BBB ip address using ifconfig command
  Extract the bbb_prebuilt.tar.gz that is passed from Ubuntu
  Connect the BBB the network and connect the collector Launchpad to the BBB

## Slide 10: Implementation Details
Steps used in Design for BBB Continued
  Check if the Launchpad is enumerated
  Enter the prebuilt folder
  Run the run_demo.sh application
  Copy the url into the browser

## Slide 11: Actual project set-up
Screenshot of the project will all components

## Slide 12: Demo
Just the Two Launchpads communicating:
  https://youtu.be/lhAG0SOZAZ0

## Slide 13: Results and Conclusions
Show screenshot of outcomes
Screenshot of CC1350 communication